Seasonal changes in the abundance, distribution, and patchiness of zooplankton and fish in four peri-alpine lakes in the Sierra Nevada, California

Samuel S. Urmy and Joseph D. Warren

Target journal: L&O

Abstract
Zooplankton are recognized as a critical component of lake ecosystems. While it is well-known that their spatial distribution is often spatially patchy, this aspect of their ecology has rarely been investigated or quantified in most lakes, let alone those in remote, high-altitude locations. We used a portable, dual-frequency scientific echosounder, mounted on small boats, to map acoustic backscatter from zooplankton and fish in four peri-alpine lakes in the Sierra Nevada Mountains of California, USA: Independence Lake, Lake Tahoe, Cherry Lake, and Lake Eleanor. We also conducted net sampling to confirm the identities of the scattering organisms, and to parameterize physics-based models for their sound-scattering properties. These then allowed us to translate acoustic backscatter into estimates of total zooplankton biomass. In two of the lakes, Cherry and Eleanor, we repeated our surveys four times at seasonal intervals between fall 2013 and fall 2014. Zooplankton abundances were highest in these lakes in the spring and summer of 2014, with peak biomasses estimated at 50 t in Lake Eleanor in April and 113 t in Cherry Lake in June. Zooplankton density appeared to increase towards closer to the lakes’ main stream inlets, and, at times of year when densities were high, displayed distinct spatial patchiness. These results illustrate some of the advantages of acoustic sampling for the detection of trends and patterns in zooplankton distributions. They also highlight the presence of gradients and patchiness in the distribution of freshwater zooplankton, even in small lakes, and raise questions about the processes generating and maintaining those spatial distributions.

Introduction
Zooplankton play a number of important roles in lake ecosystems. They exert influence on water clarity and nutrient cycling through grazing on primary production. They are also the conduit through which primary production reaches larger predators such as fish, which are often of commercial, recreational, and cultural importance for humans. For the sake of conceptual clarity or computational tractibility, most models of aquatic food webs assume, explicitly or implicitly, that the spatial distributions of their component species can be ignored (Grünbaum 2012)⁠. However, this may not always be a valid assumption, since patchiness is common in nature, and large fractions of total predation can occur in very local patches over short timespans (Temming et al. 2007)⁠.
Despite the potential importance of inhomogenous zooplankton distributions, they have rarely been quantified in lakes. This is largely a consequence of sampling techniques. The most common methods for sampling zooplankton are net tows and traps. Even when closing nets are used for vertically stratified tows, spatial resolution is limited, and all nets and traps involve a degree of spatial or temporal blurring. Automated optical techniques (Finlay et al. 2007)⁠ have better spatial resolution than traps or nets, though observations are still limited to the instrument's towed path through the water, and they lose taxonomic resolution relative to direct samples.
In contrast, active acoustics (i.e., sonar) can measure the density of animals through the water column quickly and at high (sub-meter) resolution. Acoustics are regularly used to survey fish in lakes, but have rarely been used for zooplankton. This is mostly due to the fact that most lake zooplankton scatter sound very weakly at the acoustic frequencies used for fish surveys, with the notable example of some larger genera such as Mysis (Rudstam et al. 2008)⁠ and Macrohectopus (Melnik et al. 1993)⁠, and gas-bearing larvae of midges in the genus Chaoborus (Northcote 1964, Teraguchi and Northcote 1966)⁠. Only a few studies have used high-frequency (i.e. > 200 kHz) acoustics to measure the vertical or horizontal distribution of small (< 2 mm) zooplankton (Roman et al. 2001, Hembre and Megard 2003, Parks et al. 2012)⁠. Likewise, few studies in lakes have examined the joint distribution of zooplankton with their fish predators at the same fine spatial scale (Pinel-Alloul et al. 1999, Masson et al. 2001)⁠. Acoustic methods are uniquely suited to address these questions, though they do have limitations. Most importantly, echoes return only limited information on the size and identity of scattering organisms, so that direct sampling is still necessary to identify them and as ground-truth for acoustic density estimates. Acoustics is a powerful tool for measuring the distribution of zooplankton, especially when higher frequencies enable their sensitive detection (Warren et al. 2016)⁠.
If the fine-scale distribution and patchiness of zooplankton has been rarely measured in lakes in general, it has almost never been measured in lakes at high elevations. Alpine and sub-alpine lakes differ in several important ways from low-elevation lakes. They typically have lower inputs of sediment and nutrients than lowland lakes, and are clearer and more oligotrophic. As a consequence, different environmental factors, such as ultraviolet radiation, may be more important in structuring their pelagic ecosystems (Williamson et al. 2011, 2016)⁠. Alpine and sub-alpine lakes may also be more sensitive to human disturbance, including eutrophication, pH changes, deforestation, and introductions of non-native plant and animal species (Bradford et al. 1998, Knapp et al. 2001, Schabetsberger et al. 2009)⁠.
We surveyed the zooplankton and fish in three lakes in the Sierra Nevada mountains of California, USA, between autumn 2013 and autumn 2014. Our primary tool was a two-frequency acoustic system which allowed us to measure the vertical and horizontal distribution of these animals at high (meter-scale) resolution. Acoustic observations were augmented with net samples to identify the zooplankton scatterers and parameterize scattering models that allow us to convert acoustic backscatter to estimates of biomass. Differences in the vertical profiles of zooplankton and fish density were compared between lakes. We also investigated horizontal trends in zooplankton and fish density at the scale of the lake basins, and quantified their spatial patchiness using standard geostatistical models. Changes in the distributions of zooplankton and fish from one season to another were also examined. Finally, we speculate on possible dynamics generating the observed patterns.

Methods
Study lakes
Surveys were conducted in three lakes in the Sierra Nevada, namely Cherry Lake, Lake Eleanor, Independence Lake, and Lake Tahoe (Figure 1). Our main focus was on Cherry Lake and Lake Eleanor, located at the border of Yosemite National Park near 38° 0' N, 119° 52.6' W (Figure 3). Both are reservoirs of the San Francisco Public Utilities Commision. Cherry Lake is artificial, created by the damming of Cherry Creek in 1956 (Eckart 1940)⁠. Lake Eleanor was formed naturally, but enlarged and deepened by the construction of a dam in 1918 (Eckart 1940)⁠. Both lakes are approximately 1,420 m above sea level, and have areas of 6.3 km2 (Cherry) and 3.9 km2 (Eleanor). Both lakes have been stocked with fish, including rainbow trout (Onchoryncus mykiss), brown trout (Salmo trutta), and, in Cherry Lake, eastern brook trout (Salvelinus fontinalis). Cherry and Eleanor were surveyed on successive days in October 2013, April 2014, June 2014, and September 2013. In addition to our repeated surveys of Cherry and Eleanor, we surveyed Independence Lake, located at 39° 26.4' N, 120° 18.6' W, and Lake Tahoe, at 39° 10' N, 120° 0' W once each in October 2013. Independence is a natural lake 2,127 m above sea level, and 2.6 km2 in area. It has never been stocked with fish, and is one of only two lakes in the world with a self-sustaining population of Lahontan cutthroat trout, Oncorhyncus clarkii henshawi. Lake Tahoe, at 1,897 m elevation, is much larger and deeper than the other three lakes, with a surface area of 490 km2 and maximum depth of 501 m. It is also eutrophic, in contrast to the three smaller lakes, which are mesotrophic. The watersheds of the three smaller lakes are undeveloped, although portions of the Cherry and Eleanor Creek watersheds were burned during the 2013 Rim Fire (National Wildfire Coordinating Group 2013)⁠. Tahoe is bordered by several towns, with a total permanent population of approximately 50,000. All four watersheds are on granitic substrate.

Acoustic data collection
Surveys were run from outboard-powered boats trailered to each lake, and took place during daytime. Acoustic data were collected at two frequencies, 120 and 710 kHz. The 120 kHz echosounder was a Simrad ES60 with a split-beam transducer (7° beam width), which can accurately measure the target strength of individual fish in situ. The 710 kHz echosounder was a Simrad EK60 with a single-beam (2.8° beam width) transducer. This high-frequency system could detect small (<1 mm) zooplankton (Holliday and Pieper 1995, Warren et al. 2016)⁠, but its effective range was limited to approximately 30 m due to attenuation in water. Both transducers were deployed on a pole mount off the side of the survey boat at depths of approximately 30-50 cm depending on wave conditions. Both systems were calibrated on [***date***] with a tungsten carbide standard target sphere (Foote et al. 1987)⁠. Independence Lake was sampled on 20 October 2013, and Lake Tahoe was sampled on 21 October. Cherry Lake and Lake Eleanor were each sampled four times. Cherry was sampled on 29 October 2013, and on 2 April, 24 June, and 10 September 2014. Eleanor was sampled one day later, on 30 October 2013, and 3 April, 25 June, and 11 September 2014. In the three smaller lakes, we attempted to perform a lengthwise transect from one end of the lake to the other. In Independence Lake, we were also able to add a series of zig-zag transects across the main axis of the lake. The April 2014 transects in Cherry and Eleanor were cut shorter due to snowfall, which required slow travel on the mountain roads and shortened the time available for sampling.

 Zooplankton sampling and target strength models
Zooplankton were collected on each sampling day with a vertical tow from 50 m to the surface using a 0.75 m diameter net with 80 μm mesh and preserved for later analysis in 10% buffered formalin. A subsample of 200-300 animals was split from each original sample and counted under a compound microscope. Animals were identified to the lowest possible taxonomic level. In addition, the lengths of first 30 animals counted were measured to the nearest 0.1 mm.
To convert acoustic backscatter to animal densities it is necessary to know the backscattering cross-section, σBS, of the scattering organisms. The backscattering cross-section is also expressed in its logarithmic form, the target strength, TS = 10 log10(σBS) (MacLennan et al. 2002)⁠. We calculated these values using the stochastic distorted-wave born approximation (DWBA, Stanton et al. 1998, McGehee et al. 1998)⁠, implemented as a package, SDWBA.jl (Urmy 2016)⁠ in the Julia Language (Bezanson et al. 2012)⁠. This package uses generic models for the body shapes of cladocerans and calanoid copepods from Warren et al. (2016)⁠, and we assumed “typical” density and sound-speed contrasts of 1.04 (Stanton and Chu 2000)⁠. For each lake, sampling date, and taxonomic group (i.e., cladocerans and copepods), we calculated the mean body length and its standard deviation (s.d). We then drew 1000 random lengths from a normal distribution with these parameters, scaling the generic body shape each one and calculating its backscattering cross-section. Assuming that the mean of these values, 〈σBS〉, is representative for the taxonomic group in question, then the density of animals ρ (number m-3) is given by

%rho = s_v over langle %sigma_BS rangle ,	(1)

where sv is the acoustic volume backscattering coefficient (MacLennan et al. 2002)⁠.

Acoustic data processing and analysis
Acoustic data were preprocessed using Echoview Software version 7.0 (Myriax Pty Ltd 2016)⁠. Background noise was estimated and subtracted following (De Robertis and Higginbottom 2007)⁠. Data were manually scrutinized to correct bottom lines, exclude echoes from instrument casts, and eliminate intermittent interference, such as multipath and sidelobe echoes from the steep rocky sides of the lake. Acoustic data were integrated in bins 1 m deep and 10 m wide along-track and exported for further analysis. Single fish targets were detected in the 120 kHz data using Echoview's individual target detection operator (split-beam method 1), using an uncompensated TS threshold of -70 dB, pulse length determination level of -6 dB, and minimum and maximum normalized pulse lengths of 0.5 and 2.0. Targets were rejected if their beam-pattern compensation was greater than 6 dB or if their angular standard deviation was greater than 0.5°. In Independence Lake, only the 710 kHz single-beam echosounder was operated, so we used a single-beam target detection algorithm in Echoview (single-beam method 1).
After exporting, volume backscatter due to fish was eliminated from the 710 kHz data by excluding cells where backscatter was higher at 120 kHz. Backscatter at 710 kHz in each lake on each sampling date was apportioned to copepods and cladocerans based on the proportional abundances and target strengths using the following two relations:
s_v = %rho_1 langle %sigma_{BS,1} rangle + %rho_2 langle %sigma_{BS,2} rangle
%rho_1 over %rho_2 = N_1 over N_2
where N1 and N2 are the counts of copepods and cladocerans in the corresponding net sample. Numerical densities were converted to biomassses based on the measured lengths of the zooplankton in the net samples, using published regressions for calanoid nauplii, the calanoid Diaptomus oregonenis, and Daphnia galeatea (Culver et al. 1985)⁠. Fish densities were calculated from the integrated 120 kHz backscatter. Integration cells were classified as fish if their backscatter was higher at 120 kHz than at 710 kHz. The empirical mean TS of the individual fish targets was used to convert backscatter to fish densities.

Distribution of zooplankton and fish
Vertical profiles of fish and zooplankton density were constructed for each lake and date by averaging values horizontally within each depth bin. We also investigated horizontal spatial trends and patchiness of fish and zooplankton by averaging their densities vertically through the water column. The densities in this horizontal dataset were log10-transformed and regressed on their distance from the shoreline and from each lake's main stream inlet. This was done to test whether there was any spatial trend in the density of zooplankton, e.g. in response to a supply of food or nutrients via runoff. Spatial autocorrelation was assessed by calculating empirical variograms for the residuals of each regression. Lake Tahoe was omitted from these spatial analyses, both because it is fed by many small streams at inlets around its perimeter, and, more importantly, the sampling schedule did not permit extended transects, precluding the calculation of variograms.

Results
The zooplankton communities of the four lakes differed, both between lakes and, in the case of the repeated samples at Cherry and Eleanor, over time. Lake Tahoe’s zooplankton were numerically dominated by the calanoid copepods Leptodiaptomus tyrelli (56%) and Epischura nevadensis (22%), with another 20% made up by unidentified copepods and copepodites (Figure 4). The zooplankton in Independence Lake were split evenly between the cyclopoid copepod Diacyclops thomasi (46%) and the cladoceran Daphnia middendorffiana (44%), with the remainder composed of Bosmina longirostris (6%) and unidentified rotifers (4%).
The zooplankton communities in Cherry Lake and Lake Eleanor were more diverse than those in Independence and Tahoe, with 4-10 species present in each sample (Figure 5). In October 2013, both the community in both lakes was approximately 60% cladocerans in the genera Daphnia and Diplostraca. The following April, the community in Cherry Lake remained similar, but in Lake Eleanor it had shifted to 59% Copepods, mostly Epischura nevadensis. During the final two surveys, in June and September 2014, the communities in both lakes were between 59 and 77% copepods, a large proportion of which were copepodites of unknown calanoid species. The 22-41% of the communities composed of cladocerans in June and September were again a mix of Daphnia and Diplostraca (Figure 5).
Target strengths for the different classes of zooplankton scatterers, as calculated using the DWBA, varied widely (Table 1). The strongest scatterers were copepods in Cherry Lake in April 2014, with an average TS of -111 dB. The weakest were nauplius larvae in Cherry Lake in October 2013, with a mean TS of -148 dB. Cladoceran target strengths fell between -112 and -127 dB. Adult copepod target strengths fell in the same broad range, from -104 to -128 dB. Nauplii, due to their much smaller size, were predicted to scatter sound more weakly, with their mean TS falling between -120 and -148 dB (Table 1). There were no systematic trends in TS between the lakes, or through time.
Zooplankton biomass densities were low (< 1 g m-3) in all lakes, but varied seasonally (Figure 6). In October 2013, the zooplankton density in all four lakes was low, with less than 10 mg of zooplankton biomass m-3. Lake Eleanor had a weak sound-scattering layer extending from the surface to 15 m, corresponding to an estimated peak zooplankton density of just over 6 mg m-3. In April 2014, Cherry Lake again contained zooplankton at similarly low densities, though Lake Eleanor had a zooplankton layer near the surface, increasing from near-zero density at 10 m depth to a maximum of 750 mg m-3 at 2 m depth, the bottom of the echosounder’s blind zone (Figure 6). Two months later, this layer was still present, though only about 20% as dense (maximum 130 mg m-3) as in April. During this time, a similar layer had also appeared in Cherry Lake, with a maximum density, at 2 m depth, of 371 mg m-3. By September, the surface zooplankton layer in Cherry Lake had mostly disappeared. The layer in Lake Eleanor was much less dense (maximum 91 mg m-3) and slightly deeper, with its lower limit at approximately 11 m depth (Figure 6).
When integrated from 2 m to 25 m depth and scaled by their respective lake areas, these densities yielded a wide range of estimates for the total zooplankton biomass in the different lakes. In October 2013, Lake Tahoe contained an estimated 8 t of small zooplankton. Zooplankton in the three smaller lakes was 40-70 times denser than in Tahoe, but their much smaller areas led to total biomass estimates smaller by a factor of two (Table 3). In April 2014, the zooplankton density in Lake Eleanor had increased to 13 mg m-3, raising its total biomass estimate to over 50 t, higher than that of Lake Tahoe in October 2013. Total zooplankton biomass in Cherry Lake in April was slightly less than in the October survey. By June, however, it had increased dramatically, to 113 t, while the zooplankton biomass in Eleanor dropped to 40 t. During the September 2014 survey, zooplankton populations in both lakes had dropped back to levels similar to those measured the previous autumn (Table 3).
With the exception of Cherry Lake in the first survey and Lake Eleanor in the last, zooplankton biomass density consistently increased closer to each lake’s inlet (Figure 8). This trend was most pronounced in Cherry Lake in June 2014, where zooplankton biomass density was an order of magnitude higher near the lake’s inlet than near the dam at the other end. The residuals from these regressions were spatially autocorrelated in some, but not all, lakes and surveys. In September 2013, when biomass densities in all lakes were low, none showed strong evidence for spatial structure: all three empirical variograms were relatively flat, and in Cherry and Independence Lake, were even higher at shorter lags, suggesting short-range anticorrelation. In April, when biomass in Lake Eleanor was higher, spatial structure was in evidence, with the variogram showing a sill of around 0.05 at a range of 0.5 km. Back-transformed to linear units, this implies an expected difference in biomass on the order of 12% across distances of 500 m or greater.	In June, the sill of the variogram in Lake Eleanor had increased to 0.15 at a range of 1.2 km (Figure 9), implying an expected difference in biomass on the order of 40% when transformed back to linear units. In Cherry Lake, the variogram was similar to the variogram in Eleanor from the previous survey (Figure 9). The variogram for Lake Eleanor did not change greatly between June and August 2014. However, the variogram for Cherry Lake in the final survey showed higher overall variability, which increased through the maximum lag of 2 km with no clear sign of a sill. This is trend is indicative of nested scales of patchiness. These variogram sill values, indicating the expected absolute differences between biomass densities at widely separated locations, ranged from approximately 0.05 to 0.5. These values are in log10-transformed units, so in the linear domain they imply multiplicative differences (×/÷) in zooplankton density from 0.8 to 3 at long ranges. For zooplankton in these lakes, “long ranges” as defined by the variograms are between 500 and 1500 m.

Discussion
A spring bloom of zooplankton appeared to occur in both Cherry Lake and Lake Eleanor, with peak biomass densities of 4-6 g m-3. In spring and summer, the zooplankton were concentrated in the upper 5-10 m of the water column, probably associated with a stratified surface layer. In 2014, the bloom appeared to begin earlier in Lake Eleanor than in Cherry Lake, since a near-surface zooplantkon layer was present in Eleanor, but not Cherry, during the early April survey. By June, both lakes had similar zooplankton densities, and by September, zooplankton populations in both lakes had declined by an order of magnitude. At this point there were still more zooplankton in Cherry Lake, however, suggesting that the bloom there, which started later, also took longer to collapse in the fall. This pattern, of a spring and summer increase in zooplankton as they respond to blooming phytoplankton, is consistent with standard models of seasonal cycles in lake ecosystems (Sommer et al. 1986)⁠. However, it should be noted that our seasonal sampling interval may have caused us to miss shorter-scale varibility in zooplankton populations, due either to sub-seasonal population dynamics, or responses to environmental forcings such as runoff from rainstorms or overturning due to wind. It also goes without saying that this study only covers one year, leaving longer-term trends unknown.
In all three small lakes, there was an predominant trend of increasing zooplankton density nearer to the lake’s main stream inlet. One reasonable explanation for this trend is that the streams transport nutrients, detritus, or other exogenous resources into the lake near its inlet, supporting higher production and maintaining a higher rate of zooplankton growth at the upstream end of the lake. Alternatively, the higher biomass estimates near the inlets could be an artifact due to acoustic scattering from suspended sediments introduced by the streams (Thorne and Hanes 2002)⁠. This explanation is consistent with the steeper gradients observed in June, near the peak of the seasonal snow melt and runoff.
Even after subtracting the lake-scale trend in zooplankton density, spatial autocorrelation was often evident in the residuals, as illustrated by the empirical variograms (Figure 9). These should be interpreted with caution, since they were based in most cases on single reciprocal transects down the main axis of each lake which may not have captured any spatial anisotropy present. In particular, the restricted time available to survey Cherry Lake on 2 April 2013 meant that the transect was only about 1 km long, limiting our ability to draw conclusions about the spatial distribution of zooplankton. Regardless, most of the variograms did show evidence of spatial patchiness in the distribution of zooplankton, with approximate spatial scales, based on the variogram ranges, between 500 and 2000 km. It is unknown what processes generate and maintain patchiness in these lakes. In the ocean, patchiness in zooplankton appears to be driven mostly by bottom-up processes, with scales of biological variability mirroring scales of physical variability (Denman et al. 1977, Mackas et al. 1985, Urmy et al. 2012)⁠. It seems unlikely that these lakes (with the possible exception of Tahoe) are large enough to support much horizontal physical variability, so the patchiness in the zooplankton is probably due to other processes, such as aggregation (Byron et al. 1983)⁠ or predation by schooling fish.
The acoustic methods used here offer a number of advantages over traditional direct sampling methods, though they also come with their own uncertainties and caveats. Identification of scatterers is often a challenge with acoustics. However, using a two (or more) frequency system, as in this study, reliably separates areas of backscatter from zooplankton and fish. Furthermore, direct net sampling of the zooplankton community, especially in relatively small lakes such as Independence, Cherry, and Eleanor, lets us confidently identify the main classes of zooplankton scatterers. The main source of uncertainty when interpreting acoustic backscatter as an estimate of biomass density is in the target strengths assumed for the scattering organisms. The DWBA is an accurate and widely used method to calculate zooplankton target strengths, but it in turn depends, sensitively, on accurate values for the scatterers’ material properties—namely the density- and sound-speed-contrasts g and h. To our knowledge, these values have never been measured for any freshwater zooplankton. In their absence, we used generic values from the literature, based on marine zooplankton (Stanton and Chu 2000)⁠. These values are reasonable defaults, but they may not be accurate for the species considered here, introducing a degree of unknown error into the TS and hence biomass estimates. Measurements of the material properties of freshwater zooplankton would be a worthwhile objective for future research.
Despite these uncertainties, acoustic methods for surveying zooplankton have several advantages. Acoustics can sample large volumes of water quickly at high spatial resolution, revealing trends in the distribution of zooplankton that would be missed by traditional sampling methods (Pinel-Alloul et al. 1999, Hembre and Megard 2003)⁠. In this case, these included significant trends in zooplankton biomass density with distance from shore or from the stream inlet. Accounting for spatial trends and patchiness reduces uncertainty in the biomass estimates Acoustic methods also provide high-resolution vertical profiles of fish and zooplankton densities, offering insights into the biotic and abiotic processes structuring lake ecosystems (Beauchamp et al. 1999, Urmy et al. 2016)⁠. Acoustics are also an excellent method for recording the diel vertical migration of lake zooplankton (Warren et al. 2016)⁠. Although DVM was not part of this study, it would be a worthwhile topic for further investigation in these lakes.
Table 1. Acoustic properties of crustacean zooplankton. For each class of scatterers (Cladocerans, Copepods, and Nauplius larvae), the mean acoustic target strength (dB re m2) and individual weight (μg) are displayed, along with the percentage of the net catch made up of that class of scatterers.

Table 2. Average TS of fish targets in each survey.
Lake	2013-10	2013-04	2014-06	2014-09
Cherry	-37	-41	-41	-41
Eleanor	-40	-39	-39	-38
Indepenence	-52
Tahoe	-37

Table 3. Estimated total biomass of zooplankton (in tons) in each lake, by date.
	2013-10	2014-04	2014-06	2014-09
Cherry	4.5	3.5	116	2.7
Eleanor	4.0	54	41	1.1
Independence	1.8	—	—	—
Tahoe	8.1	—	—	—

Figures

Figure 1. Map of California in the western United States, showing locations of the four study lakes.

Figure 2. Acoustic survey tracks in a) Independence Lake on 21 October 2013, and b) Lake Tahoe on 20 October 2013.

Figure 3. Tracklines of repeated acoustic surveys in Cherry Lake (left) and Lake Eleanor (right) in October 2013, April 2014, June 2014, and September 2014.

Figure 4. Composition of crustacean zooplankton community in Independence Lake and Lake Tahoe in October 2013.

Figure 5. Composition of crustacean zooplankton community in Cherry Lake and Lake Eleanor in four seasonal surveys.

Figure 6. Depth profiles of zooplankton density in the lakes sampled during each of four seasonal surveys (Lake Tahoe and Independence Lake were only sampled in October 2013). Lines show approximate biomass density of all zooplankton as a function of depth, calculated from acoustic backscatter using an estimate average target strength for the zooplankton communities. Note differing x-axis scales in each plot.

Figure 7. Depth profiles of fish density in the lakes sampled during each of four seasonal surveys (Lake Tahoe and Independence Lake were only sampled in October 2013). Lines show approximate numerical density (number per 1000 m3) of fish as a function of depth, calculated from acoustic backscatter using the average target strength measured in situ during each survey. Note differing x-axis scales in each plot.

Figure 8. Empirical variograms of log-transformed zooplankton areal biomass density (i.e., mass of zooplankton per m2 of lake surface) for each lake and survey.
References
Beauchamp, D. A., C. Baldwin, J. Vogel, and C. Gubala. 1999. Estimating diel, depth-specific foraging opportunities with a visual encounter rate model for pelagic piscivores. Canadian Journal of Fisheries and Aquatic Sciences 56:128–139.
Bezanson, J., S. Karpinski, V. B. Shah, and A. Edelman. 2012. Julia: A Fast Dynamic Language for Technical Computing. arXiv preprint:1–27.
Bradford, D. F., S. D. Cooper, T. M. Jenkins, Jr., K. Kratz, O. Sarnelle, and A. D. Brown. 1998. Influences of natural acidity and introduced fish on faunal assemblages in California alpine lakes. Canadian Journal of Fisheries and Aquatic Sciences 55:2478–2491.
Byron, E. R., P. T. Whitman, and C. R. Goldman. 1983. Observation of copepod swarms in Lake Tahoe. Limnology and Oceanography 28:378–382.
Culver, D. a., M. M. Boucherle, D. J. Bean, and J. W. Fletcher. 1985. Biomass of Freshwater Crustacean Zooplankton from Length–Weight Regressions. Canadian Journal of Fisheries and Aquatic Sciences 42:1380–1390.
Denman, K., A. Okubo, and T. Platt. 1977. The chlorophyll fluctuation spectrum in the sea. Limnology and Oceanography 22:1033–1038.
Eckart, N. A. 1940. The Water Supply System of San Francisco. Journal (American Water Works Association) 32:751–794.
Finlay, K., B. E. Beisner, and a J. D. Barnett. 2007. The use of the Laser Optical Plankton Counter to measure zooplankton size, abundance, and biomass in small freshwater lakes. Limnology and Oceanography-Methods 5:41–49.
Foote, K. G., H. P. Knudsen, G. Vestnes, D. N. MacLennan, and E. J. Simmonds. 1987. Calibration of acoustic instruments for fish density estimation: a practical guide. techreport.
Grünbaum, D. 2012. The logic of ecological patchiness. Interface Focus 2:150–155.
Hembre, L. K., and R. O. Megard. 2003. Seasonal and diel patchiness of a Daphnia population: An acoustic analysis. Limnology and Oceanography 48:2221–2233.
Holliday, D. Van, and R. E. Pieper. 1995. Bioacoustical oceanography at high frequencies. ICES Journal of Marine Science 52:279–296.
Knapp, R. A., K. R. Matthews, and O. Sarnelle. 2001. Resistance and Resilience of Alpine Lake Fauna to Fish Introductions. Ecological Monographs 71:401–421.
Mackas, D. L., K. L. Denman, and M. R. Abbott. 1985. Plankton patchiness: biology in the physical vernacular. Bulletin of Marine Science 37:652–674.
MacLennan, D. N., P. G. Fernandes, and J. Dalen. 2002. A consistent approach to definitions and symbols in fisheries acoustics. ICES Journal of Marine Science 59:365–369.
Masson, S., N. Angeli, J. Guillard, and B. Pinel-Alloul. 2001. Diel vertical and horizontal distribution of crustacean zooplankton and young of the year fish in a sub-alpine lake: an approach based on high frequency sampling. Journal of Plankton Research 23:1041–1060.
McGehee, D. E., R. L. O’Driscoll, and L. V. M. Traykovski. 1998. Effects of orientation on acoustic scattering from Antarctic krill at 120 kHz. Deep-Sea Research II 45:1273–1294.
Melnik, N. G., O. A. Timoshkin, V. G. Sidleva, S. V. Pushkin, and V. S. Mamylov. 1993. Hydroacoustic measurement of the density of the Baikal macrozooplankter Macrohectopus branickii. Limnology and Oceanography 38:425–434.
Myriax Pty Ltd. 2016. Echoview. Hobart, Tasmania.
National Wildfire Coordinating Group. 2013. Rim Fire Final Update.
Northcote, T. G. 1964. Use of a high-frequency echo sounder to record distribution and migration of Chaoborus larvae. Limnology and Oceanography 9:87–91.
Parks, S. E., J. D. Warren, K. Stamieszkin, C. a Mayo, and D. Wiley. 2012. Dangerous dining: surface foraging of North Atlantic right whales increases risk of vessel collisions. Biology letters 8:57–60.
Pinel-Alloul, B., C. Guay, N. Angeli, P. Legendre, P. Dutilleul, G. Balvay, D. Gerdeaux, and J. Guillard. 1999. Large-scale spatial heterogeneity of macrozooplankton in Lake of Geneva. Canadian Journal of Fisheries and Aquatic Sciences 56:1437–1451.
De Robertis, A., and I. Higginbottom. 2007. A post-processing technique to estimate the signal-to-noise ratio and remove echosounder background noise. ICES Journal of Marine Science 64:1282–1291.
Roman, M. R., D. V. Holliday, and L. P. Sanford. 2001. Temporal and spatial patterns of zooplankton in the Chesapeake Bay turbidity maximum. Marine Ecology Progress Series 213:215–227.
Rudstam, L. G., F. R. Knudsen, H. Balk, G. Gal, B. T. Boscarino, and T. Axenrot. 2008. Acoustic characterization of Mysis relicta at multiple frequencies. Canadian Journal of Fisheries and Aquatic Sciences 65:2769–2779.
Schabetsberger, R., M. S. Luger, G. Drozdowski, and A. Jagsch. 2009. Only the small survive: Monitoring long-term changes in the zooplankton community of an Alpine lake after fish introduction. Biological Invasions 11:1335–1345.
Sommer, U., Z. M. Gliwicz, W. Lampert, and A. Duncan. 1986. The PEG-model of seasonal succession of planktonic events in fresh waters. Archiv für Hydrobiologie 106:433–471.
Stanton, T. K., and D. Chu. 2000. Review and recommendations for the modelling of acoustic scattering by fluid-like elongated zooplankton: euphausiids and copepods. ICES Journal of Marine Science 57:793–807.
Stanton, T. K., D. Chu, and P. H. Wiebe. 1998. Sound scattering by several zooplankton groups. II. Scattering models. The Journal of the Acoustical Society of America 103:236–253.
Temming, A., J. Floeter, and S. Ehrich. 2007. Predation Hot Spots: Large Scale Impact of Local Aggregations. Ecosystems 10:865–876.
Teraguchi, M., and T. G. Northcote. 1966. Vertical distribution and migration of Chaoborus larvae in Corbett Lake, British Columbio. Limnology and Oceanography 11:164–176.
Thorne, P. D., and D. M. Hanes. 2002. A review of acoustic measurement of small-scale sediment processes. Continental Shelf Research 22:603–632.
Urmy, S. S. 2016. SDWBA.jl: A Julia package for modeling acoustic backscatter from zooplankton.
Urmy, S. S., J. K. Horne, and D. H. Barbee. 2012. Measuring the vertical distributional variability of pelagic fauna in Monterey Bay. ICES Journal of Marine Science 69:184–196.
Urmy, S. S., C. E. Williamson, T. H. Leach, S. G. Schladow, E. P. Overholt, and J. D. Warren. 2016. Vertical redistribution of zooplankton in an oligotrophic lake associated with reduction in ultraviolet radiation by wildfire smoke. Geophysical Research Letters 43:3746–3753.
Warren, J. D., T. H. Leach, and C. E. Williamson. 2016. Measuring the distribution, abundance, and biovolume of zooplankton in an oligotrophic freshwater lake with a 710 kHz scientific echosounder. Limnology and Oceanography: Methods.
Williamson, C. E., J. M. Fischer, S. M. Bollens, E. P. Overholt, and J. K. Breckenridge. 2011. Towards a more comprehensive theory of zooplankton diel vertical migration: Integrating ultraviolet radiation and water transparency into the biotic paradigm. Limnology and Oceanography 56:1603–1623.
Williamson, C. E., E. P. Overholt, J. A. Brentrup, R. M. Pilla, T. H. Leach, S. G. Schladow, J. D. Warren, S. S. Urmy, S. Sadro, S. Chandra, and P. J. Neale. 2016. Sentinel responses to droughts, wildfires, and floods: Ultraviolet radiation and the consequences for lakes and their ecosystem services. Frontiers in Ecology and the Environment 14:102–109.